Replace sdX in the following instructions with the device name for the SD card as it appears on your computer.
Prerequisites: Raspberry Pi 2, Raspberry Pi Zero, PC running linux, USB microSD card reader, internet.
These instructions are for the IOTHERMOSTAT project, but are generic. Simply replace IOTHERMOSTAT with your own name.
Instructions largely copied from https://archlinuxarm.org/platforms/armv6/raspberry-pi

1. Start fdisk to partition the SD card:
  fdisk /dev/sdX
2. At the fdisk prompt, delete old partitions and create a new one:
  1. Type o. This will clear out any partitions on the drive.
  2. Type p to list partitions. There should be no partitions left.
  3. Type n, then p for primary, 1 for the first partition on the drive, press ENTER to accept the default first sector, then type +100M for the last sector.
  4. Type t, then c to set the first partition to type W95 FAT32 (LBA).
  5. Type n, then p for primary, 2 for the second partition on the drive, and then press ENTER twice to accept the default first and last sector.
  6. Write the partition table and exit by typing w.
3. Create and mount the FAT filesystem:
  mkfs.vfat /dev/sdX1
  mkdir boot
  mount /dev/sdX1 boot
4. Create and mount the ext4 filesystem:
  mkfs.ext4 /dev/sdX2
  mkdir root
  mount /dev/sdX2 root
5. Download and extract the root filesystem (as root, not via sudo):
  wget http://os.archlinuxarm.org/os/ArchLinuxARM-rpi-latest.tar.gz
  bsdtar -xpf ArchLinuxARM-rpi-latest.tar.gz -C root
  sync
6. Move boot files to the first partition:
  mv root/boot/* boot
7. Copy cmdline.txt and config.txt to boot.
8. Copy waveshare35a-overlay.dtb to boot/overlays
9. Copy reconnnect.sh to root
10. Unmount the two partitions:
  umount boot root
11. Insert the SD card into a Raspberry Pi 2, connect ethernet, and power up.
12. Use the serial console or SSH to the IP address given to the board by your router.
  1. Login as the default user alarm with the password alarm.
  2. The default root password is root.
13. Configure mirrors:
    nano /etc/pacman.d/mirrorlist
14. Configure time and localization:
    timedatectl set-ntp true
    timedatectl set-timezone Europe/Amsterdam
    echo "en_US.UTF-8 UTF-8" >> /etc/locale.gen
    locale-gen
    echo "LANG=en_US.UTF-8" > /etc/locale.conf
15. Initialize the pacman keyring and populate the Arch Linux ARM package signing keys:
  touch /root/.gnupg/dirmngr_ldapservers.conf
  pacman -Scc && rm /var/lib/pacman/sync/* && rm -rf /etc/pacman.d/gnupg

  pacman-key --init
  pacman -S archlinux-keyring
  pacman -Sy
  pacman-key --populate archlinuxarm
  pacman-key --refresh-keys
  pacman -Syu sudo
16. setup iothermostat user

    useradd -m -s /bin/bash iothermostat
    passwd iothermostat (default iothermostat2018).
    su
    visudo
    (under root ALL=(ALL) ALL add line, after pressing ‘i’):
      iothermostat ALL=(ALL) ALL
    (to quit, press ESC :wq RETURN)
    reboot now
    (reconnect with ssh user iothermostat)
    sudo userdel alarm
17. Install rtl8188eu dkms driver from AUR:
  sudo pacman -Syu git base-devel linux-headers
  sudo echo “blacklist r8188eu” > /etc/modprobe.d/nokernelwifi.conf
  mkdir builds
  cd builds
  git clone https://aur.archlinux.org/8188eu-dkms.git
  cd 8188eu-dkms
  makepkg -sirc
18. Setup NetworkManager
    su
    pacman -Syu networkmanager dnsmasq
    hostnamectl set-hostname iothermostat
    echo "dhcp-range=10.0.0.1,10.0.0.2,12h" >> /etc/dnsmasq.conf
    systemctl stop systemd-networkd.service
    systemctl disable systemd-networkd.service
    systemctl start NetworkManager.service
    systemctl enable NetworkManager.service
19. Plug in the USB Wifi dongle. Create the fallback hotspot:
  nmcli -s dev wifi hotspot con-name IOTHERMOSTAT ssid IOTHERMOSTAT password iothermostat0
  (Ctrl+C)
  nmcli connection mod IOTHERMOSTAT wifi.hidden no
  nmcli connection mod IOTHERMOSTAT connection.autoconnect yes
  nmcli connection mod IOTHERMOSTAT connection.autoconnect-priority -10
  shutdown now
20. Plug memory card + wifi dongle into hestia pi touch. Boot. Connect to IOTHERMOSTAT hotspot with password iothermostat0. Ssh into server ip (password: iothermostat2018):
  ssh iothermostat@10.42.0.1
21. Configure network for user
    sudo ./reconnect.sh YOURSSID 'YOURPASSPHRASE'
22. Connect to YOURSSID, find the ip of iothermostat (see display) and ssh to iothermostat@ip
23. Installation
    su
    pacman -Syu pwgen rng-tools i2c-tools lm_sensors wget pacman-contrib
    echo RNGD_OPTS="-o /dev/random -r /dev/hwrng” > /etc/conf.d/rngd
    systemctl stop haveged.service
    systemctl disable haveged.service
    systemctl start rngd.service
    systemctl enable rngd.service
  # enable i2c
  echo i2c-dev >> /etc/modules-load.d/raspberrypi.conf
  echo i2c-bcm2708 >> /etc/modules-load.d/raspberrypi.conf
24. Ctrl+D, install fake-hwclock-git:
    mkdir /home/iothermostat/builds
    cd /home/iothermostat/builds
    git clone https://aur.archlinux.org/fake-hwclock-git.git
    cd fake-hwclock
    nano PKGBUILD, add # in front of depends=(‘’)
    makepkg -sirc
    cd ..
    systemctl start fake-hwclock
    systemctl enable fake-hwclock
25. Clean up:
  sudo journalctl --flush –rotate
  sudo journalctl –vacuum-time=1seconds
  sudo reboot now
26. Install python-raspberry-gpio:
    cd /home/iothermostat/builds
  git clone https://aur.archlinux.org/python-raspberry-gpio.git
  cd python-raspberry-gpio
  makepkg -sirc
  cd ..